## Slide 1
ESTUARY TRENDS: WEATHER & WATER QUALITY
Resilient estuaries and coastal watersheds -where human and natural communities thrive.
North Carolina National Estuarine Research Reserve (NERR)
This reserve was established to preserve the fragile natural areas that make up the third largest estuarine system in the country and the variety of life found there. The reserve is comprised of four sites that represent the two major biogeographic regions located north (Virginian) and south (Carolinian) of Cape Hatteras. The Currituck Banks site is in the Virginian, while Rachel Carson, Masonboro Island, and Zeke’s Island are Carolinian. For more information go to:
http://www.nccoastalreserve.net/
2016 HIGHLIGHTS
It was dryer - rainfall was below average compared to the long-term historical average
It was hotter – summer/fall air temperatures were higher than the long-term historical average
Dissolved inorganic nitrogen (DIN) was in the good to fair range for all locations
Algal blooms occurred in the spring and summer at East Cribbing and Zeke's Basin locations

## Slide 2
HOW IS OUR ESTUARY CHANGING?
Precipitation is not changing
Air Temperature is increasing
Nitrogen (ammonium ) is decreasing at all locations
Algae growth is increasing at all locations
Dissolved Oxygen is decreasing at three out of four locations
Trends in Weather & Water Quality*
*Based on data collected from 2007-2016
North Carolina Sampling Locations
Weather Can Have A Major Impact On Water Quality
Precipitation & Air Temperature
Rainfall was ~20 inches less than the long-term historical average in 2016
Air Temperature was hotter in March and in the summer/fall of 2016 compared to the long-term historical average
Location ID | Location Name
RC | Research Creek
Air Temperature | Precipitiation
h | —
Location ID | Location Name
EC | East Cribbing
LC | Loosin Creek
RC | Research Creek
ZB | Zeke's Basin
Water Temperature | Salinity | Dissolved Oxygen | pH | Turbidity
— | i | — | i | h
h | — | i | i | i
— | — | i | i | i
— | i | i | i | h
Location ID | Location Name
EC | East Cribbing
LC | Loosin Creek
RC | Research Creek
ZB | Zeke's Basin
Ortho-phosphate | Ammonium | Nitrite | Nitrate | Chlorophyll-a
— | i | — | — | h
— | i | h | x | h
— | i | h | x | h
— | i | — | — | h

## Slide 3
Do We Have Too Many Nutrients In The Water?
Phytoplankton (also called microalgae) are tiny, plant-like organisms that need nutrients (nitrogen and phosphorus) to grow. Phytoplankton are critical to estuarine and ocean health. However, some conditions, such as excess nutrients, can cause phytoplankton blooms. The blooms can decrease the dissolved oxygen underwater life needs to survive, negatively impact human health, and close fishery harvest areas.
Nitrogen
Dissolved inorganic nitrogen (DIN) is the type of nitrogen in the water phytoplankton need to grow. At North Carolina NERR, data show that DIN concentrations are not changing over the long-term. All of the measurements are in the fair to good range. The critical threshold of 0.5 mg/L has not been exceeded at any sampling location.
Algae
Phytoplankton growth is measured by chlorophyll a concentrations. At North Carolina NERR, data show that chlorophyll a levels are increasing the long-term. Measurements are in the poor to good range. Concentrations exceed the critical threshold of 20 ug/L, at times, at three out of four sampling locations. Concentrations most often exceed the critical threshold at Zeke's Basin.
How is Oxygen Changing?
Dissolved oxygen decreased at Loosin Creek, Research Creek and Zeke's Basin. Most of the measurements vary between the poor to good range at all locations.
Small Changes You Can Make To Help
Limit use of fertilizers/pesticides and apply responsibly
Use compost as fertilizer in gardens
Collect pet droppings
Plant trees and rain gardens
Redirect downspouts away from impervious surfaces like driveways and sidewalks
Wash cars and boats on lawn and not the driveway

## Slide 4
Contact NOAA
first.last@noaa.gov
(555) 555-1212