## Slide 1
ESTUARY TRENDS: WEATHER & WATER QUALITY
Resilient estuaries and coastal watersheds -where human and natural communities thrive.
San Francisco Bay National Estuarine Research Reserve (NERR)
This reserve is comprised of two areas—Rush Ranch and China Camp State Park—located 30 miles north and 50 miles northeast of San Francisco, along the salinity gradient of the San Francisco Bay. A primary focus of the reserve is supporting tidal marsh restoration through research, monitoring, and education. The reserve sites serve as valuable reference for the San Francisco region, where nearly 97 percent of the historic tidal wetlands have been lost to development. Reference sites provide a local baseline for scientific restoration activities. For more information go to:
http://www.sfbaynerr.org/
2016 HIGHLIGHTS
It was wetter - rainfall was above average compared to the long-term historical average
It was warmer – late winter and spring air temperatures were slightly higher than the long-term historical average
Dissolved inorganic nitrogen (DIN) concentrations were highest at First Mallard
An algal bloom occurred in the spring at Second Mallard

## Slide 2
HOW IS OUR ESTUARY CHANGING?
Precipitation is not changing
Air Temperature is increasing
Nitrogen (ammonium) is increasing at two out of four locations
Algae growth is decreasing at one out of four locations
Dissolved Oxygen is decreasing at two out of four locations
Trends in Weather & Water Quality*
*Based on data collected from 2007-2016
San Francisco Bay Sampling Locations
Weather Can Have A Major Impact On Water Quality
Precipitation & Air Temperature
Rainfall was ~15 inches greater than the long-term historical average in 2016
Air Temperature was warmer in the late winter/spring of 2016 compared to the long-term historical average
Location ID | Location Name
RR | Rush Ranch
Air Temperature | Precipitiation
h | —
Location ID | Location Name
CC | China Camp
FM | First Mallard
GC | Gallinas Creek
SM | Second Mallard
Water Temperature | Salinity | Dissolved Oxygen | pH | Turbidity
h | h | i | i | h
h | — | — | i | h
h | h | i | i | h
h | — | — | i | —
Location ID | Location Name
CC | China Camp
FM | First Mallard
GC | Gallinas Creek
SM | Second Mallard
Ortho-phosphate | Ammonium | Nitrite | Nitrate | Chlorophyll-a
— | h | x | — | i
h | — | x | x | —
— | h | x | — | —
— | — | x | x | —

## Slide 3
Do We Have Too Many Nutrients In The Water?
Phytoplankton (also called microalgae) are tiny, plant-like organisms that need nutrients (nitrogen and phosphorus) to grow. Phytoplankton are critical to estuarine and ocean health. However, some conditions, such as excess nutrients, can cause phytoplankton blooms. The blooms can decrease the dissolved oxygen underwater life needs to survive, negatively impact human health, and close fishery harvest areas.
Nitrogen
Dissolved inorganic nitrogen (DIN) is the type of nitrogen in the water phytoplankton need to grow. At San Francisco Bay NERR, there is not enough data to determine if DIN is changing over the long-term. Measurements are in the poor to good range. The critical threshold of 0.5 mg/L is often exceeded at First Mallard.
Algae
Phytoplankton growth is measured by chlorophyll a concentrations. At San Francisco Bay NERR, data show that chlorophyll a levels are not changing over the long-term at most locations and are decreasing at China Camp. Most of the measurements are in the fair to good range. Concentrations exceed the critical threshold of 20 ug/L, at times, at all sampling locations. Concentrations most often exceed the critical threshold at First Mallard.
How is Oxygen Changing?
Dissolved oxygen decreased at China Camp and Gallinas Creek. Most of the measurements vary between the poor to good range at all locations.
Small Changes You Can Make To Help
Limit use of fertilizers/pesticides and apply responsibly
Use compost as fertilizer in gardens
Collect pet droppings
Plant trees and rain gardens
Redirect downspouts away from impervious surfaces like driveways and sidewalks
Wash cars and boats on lawn and not the driveway

## Slide 4
Contact NOAA
first.last@noaa.gov
(555) 555-1212